## Slide 1: SMART BUOY
BRYAN MCCOMBS EE
DANIEL ROSABAL EE
MATT CROUCH PSE
JULIAN ROJAS CE
Group 11

## Slide 2: Motivation
CREOL team member
Living in Florida
  Surrounded by water
Recreational use as well as commercial use
  Boating, Fishing, Surfing
  Surveying
Notes: Br

## Slide 3: Goals and Objectives
Goal
Design a small scale, cost efficient data buoy that can be monitored through a mobile app with ease of operation
Functionality of the data buoy system
Surrounding air and water temperatures
Wind Speed
Salinity Detection
Realtime 3D Movement View
Solar Power Charging
Mobile application for easy user interface
Notes: Br

## Slide 4: Specifications
Buoy Specifications |  | 
Component | Parameter | Specification
Housing | Dimension | <20”Lx20”Wx20”H
Wireless Communication | Range | ≥20 ft
Sensor | Range | Accuracy
Wind Speed | up to 60 mph | ±1 mph
Water and Air Temperature | up to 120°F | ±1°F
Notes: Br

## Slide 5: Overall Block Diagram
Notes: Br

## Slide 6: Power System
Notes: Da

## Slide 7: Power System
Notes: Da

## Slide 8: Solar Panel
Adafruit Solar Panel
6V output at 330mA
2W
Durable and lightweight (90g)
Waterproof
Supplier | Adafruit
Product ID | 200
Size | 4.4” x 5.4”
Cost | $29
Notes: Da

## Slide 9: Battery
Lithium Polymer Battery
3.7V nominal voltage
1200mAh nominal capacity
Lightweight (22g)
Supplier | Adafruit
Product ID | 258
Size | 1.3” x 2.4”
Cost | $9.95
Notes: Da

## Slide 10: Battery Charger
Based on the MCP73871 microchip
Temperature monitoring
Three indicator LEDs
  Power
  Charging status
  Charging complete
Lightweight (5.7g)
Too dark?
Supplier | Adafruit
Product ID | 390
Size | 1.6” x 1.3”
Cost | $17.50
Notes: Da

## Slide 11: Power Converter
Based on TI’s TPS63060
3 to 12V input
5V output
90%+ operating efficiency
Lightweight (2.5g)
Supplier | Adafruit
Product ID | 2190
Size | 0.7” x 1.3”
Cost | $9.95
Notes: Da

## Slide 12: Sensors
Notes: DANI

## Slide 13: 3D Movement View
Adafruit 9-DOF Breakout
Regulated supply voltage 1.71 to 3.6 V
L3GD20H 3-axis gyroscope: ±250, ±500, or ±2000 dps scale
LSM303 3-axis compass: ±1.3 to ±8.1 gauss magnetic field scale
LSM303 3-axis accelerometer: ±2g/±4g/±8g/±16g selectable scale
I2C/SPI digital output interface
16 bit data output
Lightweight (2.8g)
Supplier | Adafruit
Product ID | 1714
Size | 1.5” x 0.9”
Cost | $19.95
Notes: DAN

## Slide 14: Wind Speed
Adafruit Anemometer
Supply Voltage 5-24V
Analog output
  0.4V (0 mph) -2.0V (72 mph)
  Every 50 mV ~ 2 mph
Accurate
  Within ±1 mph
Durable
Waterproof
Manufacturer | Adafruit
Product ID | 1733
Size | 4” x 5.6”
Cost | $44
Notes: BRY

## Slide 15: Water and Air Temperature
DS18B20 Digital Temperature Sensor
Wide range, Good accuracy
  -55° - 125° C (-67°-257°F)
  ±0.5° over -10°- 85° C range (±1°F over 50°-185°F)
Simple Implementation
  Single data wire
  Parasitic Power
  Each sensor has a unique 64 bit address
9-12 bit programmable resolution
Able to use for both functions
  Available in Waterproof Casing
Manufacturer | Adafruit
Product ID | 381
Size | T0-92
Supply | 3-5.5 V
Cost | $4
Notes: BRY

## Slide 16: Waterproof Configuration
Vcc (5V)
DATA
GND
4.7kΩ
Stainless Tubing
Heat Shrink
Connecting Wires
PVC Coating
1.2”
0.15”
Notes: BRY

## Slide 17: Water Salinity
Design a sensor that measures salt content using light
Laser Diode
Mirror
Quadrant Cell Photodiode
  Measure distance moved
Use set voltages to create ranges of salinity
Notes: MAT

## Slide 18: Water Salinity
Laser Diode
  635nm wavelength
  Visible light for alignment
Mirror
  95% reflection at chosen wavelength
Quadrant Cell Photodiode
  1.19x1.19mm Area with 0.50mm Gap
Supplier | Lightinthebox.com | Edmunds Optics | Mouser Electronics
Part | Laser Diode | Mirror | Quad Cell
Product ID | 02187190 | #46-618 | 718-QP5.8-6-TO5
Size | 6mm x 10mm | 12.5mm Diam | 9.2mm x 3.2mm
Cost | $4.99 | $22.50 | $44.54
Notes: MAT

## Slide 19: Salinity Components

## Slide 20: Salinity Sensor Configuration
Notes: MAT

## Slide 21: Microcontroller
Notes: Ju

## Slide 22: Microcontroller
Atmel ATmega328
Used in Arduino UNO Boards
23 I/O Pins
Low-Power uC
3 Timers (Interrupts)
SPI and I2C capable
Ease of use
Notes: JU

## Slide 23: Software Development
Arduino IDE
  Programming Microcontroller in C.
  Arduino Libraries.
    Adafruit and Dallas-Temperature.
  Runs on Windows and MAC OS.
  Open Source.
Android Studio IDE.
  Android Official Development Environment.
  Programming Mobile App in Java .
  XML for Android GUI.
Notes: JU

## Slide 24
Microcontroller FlowChart

## Slide 25: User Interface

## Slide 26: Wireless Communication
Notes: JULI

## Slide 27: Wireless
HC-06 Bluetooth Module
  Inexpensive.
  Ease of Use.
  Master and Slave Mode.
  Low-Power Consumption.
  Range up to 30ft
    Perfect for in the field research.
Supplier | Ebay
Size | 0.6” x 1.7”
Vcc | 3.3-5 V
I/O pins | 4 (Vcc, Gnd, Tx, Rx)
Cost | $4
Notes: JUL

## Slide 28: Printed Circuit Board
Notes: BRY

## Slide 29: Schematic
EAGLE
ATmega328
Headers for Sensors
LED’s for power and
Wireless connection
Notes: BRY

## Slide 30: Eagle Board
Second Revision
5.2 cm x 7.3 cm
Few vias
Ordered from Elecrow
  10 5x10cm for $11
  Fast Shipping
Notes: BRY

## Slide 31: Buoy Housing
Oil disposal container
Wal Mart
Water tight
Durable
Small Design
Large enough to house
all components
Notes: DANI

## Slide 32: Prototyping
Notes: DAN

## Slide 33: Breadboard Overview
Accelerometer
MCU
ATmega328p
Wireless
HC-06
LiPo Battery Charger
Buck Converter
Notes: DAN

## Slide 34: Administrative Content
Notes: MAT

## Slide 35: Work Distribution
Notes: MAT

## Slide 36: Financing
Self Financed
Initial budget of $100 per team member
Using as much personal inventory as possible
Notes: MAT

## Slide 37: Budget
Notes: MAT

## Slide 38: Future Development
Adding a counter-balance for use in rougher waters.
*Drawn using Solid Edge

## Slide 39: Issues
Notes: MAT

## Slide 40: Questions?